## Slide 1: CS 4700 Network Fundamentals
Congestion Control
(You thought we were done with TCP?)
Revised 2/22/24

## Slide 2: Transport Layer
Function:
  Demultiplexing of data streams
Optional functions:
  Creating long lived “connections”
  Reliable, in-order packet delivery
  Error detection
  Flow and congestion control
Key challenges:
  Detecting and responding to congestion
  Balancing fairness against high utilization
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 3: Outline
Congestion Basics
Original TCP
TCP Tahoe and Reno
TCP Cubic
BBR

## Slide 4: What is Congestion?
Load on the network is higher than capacity
  Capacity is not uniform across networks
    Modem vs. Cellular vs. Cable vs. Fiber Optics
  There are multiple flows competing for bandwidth
    Residential cable modem vs. corporate datacenter
  Load is not uniform over time
    9pm Sunday night = everyone streaming Netflix

## Slide 5: Why is Congestion Bad?
Results in packet loss
  Routers have finite buffers, packets must be dropped
Practical consequences
  Router queues build up, delay increases
  Wasted bandwidth from retransmissions
  Low network goodput

## Slide 6: The Danger of Increasing Load
Knee – point after which
  Throughput increases very slowly
  Delay increases quickly
In an M/M/1 queue
  Delay = 1/(1 – utilization)
Cliff – point after which
  Throughput  0
  Delay  ∞
Congestion Collapse
Load
Load
Goodput
Delay
Knee
Cliff
Ideal point

## Slide 7: Cong. Control vs. Cong. Avoidance
Congestion Collapse
Goodput
Knee
Cliff
Load
Congestion Avoidance:
Stay left of the knee
Congestion Control:
Stay left of the cliff

## Slide 8: Advertised Window, Revisited
Does TCP’s advertised window solve congestion?
NO
The advertised window only protects the receiver
A sufficiently fast receiver can max the advertised window
  What if the network is slower than the receiver?
  What if there are other concurrent flows?
Key points
  Window size determines send rate
  Window must be adjusted to prevent congestion collapse

## Slide 9: Goals of Congestion Control
Adjusting to the bottleneck bandwidth
Adjusting to variations in bandwidth
Sharing bandwidth between flows
Maximizing throughput

## Slide 10: General Approaches
Do nothing, send packets indiscriminately
  Many packets will drop, totally unpredictable performance
  May lead to congestion collapse
Reservations
  Pre-arrange bandwidth allocations for flows
  Requires negotiation before sending packets
  Must be supported by the network
Dynamic adjustment
  Use probes to estimate level of congestion
  Speed up when congestion is low
  Slow down when congestion increases
  Messy dynamics, requires distributed coordination

## Slide 11: TCP Congestion Control
Introduce a congestion window at the sender
  Congestion control is sender-side problem
  Controls the number of unACKed packets
  Separate variable, but bounded by the receiver’s advertised window
Sending rate is ~ congestion window/RTT (for Tahoe and Reno…)
  Why is the send rate proportional to RTT?
  TCP is ACK clocked
Idea: vary the window size to control the send rate

## Slide 12: Congestion Window (cwnd)
Limits how much data is in transit, denominated in bytes
wnd = min(cwnd, adv_wnd);
effective_wnd = wnd – (last_byte_sent – last_byte_acked);
last_byte_acked
last_byte_sent
cwnd
effective_wnd
adv_wnd
Bytes
To Send

## Slide 13: Outline
Congestion Basics
Original TCP
TCP Tahoe and Reno
TCP Cubic
BBR

## Slide 14: Original TCP Congestion Controller
What should be TCP’s “signal” for congestion?
Uses packet loss as a signal of congestion
  Specifically, timeouts
Uses additive increase, multiplicative decrease strategy to try and converge to fair sharing of bandwidth between flows
  Implements the famous “slow start” approach

## Slide 15: Two Basic Components
Congestion detection approach
  Packet dropping is a reliably signal
    Delay-based methods are tricky
  How do you detect packet drops? ACKs
    Timeout after not receiving an ACK
    Several duplicate ACKs in a row (in later versions, e.g., Tahoe and Reno)
Rate adjustment algorithm
  Modify cwnd
  Probe for bandwidth
  Respond to congestion
Except on wireless networks

## Slide 16: Rate Adjustment
Basic algorithm
  Upon receipt of a fresh ACK: increase cwnd
    Data was delivered, perhaps we can send faster
    cwnd growth is proportional to RTT (a.k.a. TCP is ACK clocked)
  On loss: decrease cwnd
    Data is being lost, there must be congestion
Question: what increase/decrease functions to use?

## Slide 17: Utilization and Fairness
Flow 1 Throughput
Flow 2 Throughput
Max throughput for flow 2
Zero throughput for flow 1
Max throughput for flow 1
Zero throughput for flow 2
Less than full utilization
More than full utilization (congestion)
Ideal point
Max efficiency
Perfect fairness
Equal throughput
(fairness)

## Slide 18: Multiplicative Increase, Additive Decrease
Not stable!
Veers away from fairness
Flow 1 Throughput
Flow 2 Throughput

## Slide 19: Additive Increase, Additive Decrease
Stable
But does not converge to fairness
Flow 1 Throughput
Flow 2 Throughput

## Slide 20: Multiplicative Increase, Multiplicative Decrease
Stable
But does not converge to fairness
Flow 1 Throughput
Flow 2 Throughput

## Slide 21: Additive Increase, Multiplicative Decrease
Converges to stable and fair cycle
Symmetric around y=x
Flow 1 Throughput
Flow 2 Throughput

## Slide 22: Implementing Congestion Control
Maintains three variables:
  cwnd: congestion window
  adv_wnd: receiver advertised window
  ssthresh: slow start threshold (used to update cwnd)
Two phases of congestion control
  Slow start (cwnd < ssthresh)
    Probe for bottleneck bandwidth
  Congestion avoidance (cwnd >= ssthresh)
    AIMD
For sending, use: wnd = min(cwnd, adv_wnd)

## Slide 23: Slow Start
Goal: reach knee quickly
Upon starting (or restarting) a connection
  cwnd =1
  ssthresh = adv_wnd
  Each time a segment is ACKed, cwnd++
Continues until…
  ssthresh is reached
  Or a packet is lost
Slow Start is not actually slow
  cwnd increases exponentially
Load
Goodput
Knee
Cliff

## Slide 24: Slow Start Example
1
2
3
4
5
6
7
cwnd = 1
cwnd = 2
cwnd = 4
cwnd = 8
cwnd grows rapidly
Slows down when…
  cwnd >= ssthresh
  Or a packet drops

## Slide 25: Congestion Avoidance
AIMD mode
ssthresh is lower-bound guess about location of the knee
If cwnd >= ssthresh then each time a segment is ACKed cwnd += 1/cwnd
So cwnd is increased by one segment only if all segments the previous window have been acknowledged

## Slide 26: Congestion Avoidance Example
Round Trip Times
cwnd (in segments)
Slow Start
cwnd >= ssthresh
cwnd = 1
cwnd = 2
cwnd = 4
cwnd = 8
cwnd = 9
ssthresh = 8

## Slide 27: TCP Pseudocode
Initially: cwnd = 1; ssthresh = adv_wnd;
New ACK received: if (cwnd < ssthresh) /* Slow Start*/ cwnd = cwnd + 1; else /* Congestion Avoidance */ cwnd = cwnd + 1/cwnd;
Timeout: /* Multiplicative decrease */ ssthresh = cwnd/2; cwnd = 1;

## Slide 28: The Big Picture
Time
cwnd
Timeout
Slow Start
Congestion
Avoidance
ssthresh

## Slide 29: Outline
Congestion Basics
Original TCP
TCP Tahoe and Reno
TCP Cubic
BBR

## Slide 30: Congestion Control Goals, revisited
Adjusting to the bottleneck bandwidth
Adjusting to variations in bandwidth
Sharing bandwidth between flows
Maximizing throughput
Dynamic adjustment
  Use probes (packet drops) to estimate level of congestion
  Speed up (increase cwnd quickly) when congestion is low
  Slow down (increase cwnd slowly) when congestion increases
  Requires distributed coordination (every TCP client)

## Slide 31: The Evolution of TCP
Thus far, we have discussed the original TCP congestion controller
However, TCP was invented in 1974!
  Today, there are many variants of TCP
Early, popular variants:
  TCP Tahoe (1988): fast retransmit
  TCP Reno (1990): fast recovery

## Slide 32: TCP Tahoe: Fast Retransmit
Problem: if segment is lost, there is a long wait until the RTO
Tahoe: retransmit after 3 duplicate ACKs
1
2
3
4
5
6
7
cwnd = 1
cwnd = 2
cwnd = 4
1
2
3
3
3
3
3 Duplicate ACKs

## Slide 33: TCP Reno: Fast Recovery
Initially: cwnd = 1; ssthresh = adv_wnd;
New ACK received: if (cwnd < ssthresh) /* Slow Start*/ cwnd = cwnd + 1; else /* Congestion Avoidance */ cwnd = cwnd + 1/cwnd;
3 duplicate ACKs:
/* Fast Recovery */ ssthresh = cwnd/2;
cwnd = ssthresh
Timeout:
/* Multiplicative decrease */ ssthresh = cwnd/2;
cwnd = 1;
After a fast-retransmit set cwnd =cwnd/2
  i.e., don’t reset cwnd to 1
  Avoid unnecessary return to slow start
But when RTO expires still do cwnd = 1
  Return to slow start, same as Tahoe
  Indicates packets aren’t being delivered at all
  i.e., congestion must be really bad

## Slide 34: Fast Retransmit and Fast Recovery
At steady state, cwnd oscillates just above the optimal window size
TCP always forces packet drops
Time
cwnd
Timeout
Slow Start
Congestion Avoidance
Fast Retransmit/Recovery
ssthresh
Timeout

## Slide 35: Outline
Congestion Basics
Original TCP
TCP Tahoe and Reno
TCP Cubic
BBR

## Slide 36: Many TCP Variants…
The original
  Slow start with AIMD
  Dynamic RTO based on RTT estimate
Tahoe and Reno: fast retransmit and fast recovery
NewReno: improved fast retransmit
  Each duplicate ACK triggers a retransmission
  Problem: >3 out-of-order packets causes pathological retransmissions
Vegas: delay-based congestion avoidance
And many, many, many more…

## Slide 37: TCP in the Real World
What are popular variants today?
  Key problem: TCP performs poorly on high bandwidth-delay product networks (like the modern Internet)
  Compound TCP (Windows)
    Based on Reno
    Uses two congestion windows: delay based and loss based
    Thus, it uses a compound congestion controller
  TCP CUBIC (Linux)
    Enhancement of BIC (Binary Increase Congestion Control)
    Window size controlled by cubic function
    Parameterized by the time T since the last dropped packet
  TCP BBR (Google)
  QUIC (Not really TCP)

## Slide 38: Issues with TCP
Most Internet traffic is TCP
However, many issues with the protocol
  Synchronization of flows
  Poor performance with small flows
  Problems on modern, high bandwidth-delay product networks
    Slow ramp-up when bandwidth is large, resulting in low utilization
  Lack of fairness when RTT varies across flows
  Poor performance on wireless networks, packet loss is assumed to be congestion
  Probing for bandwidth induces congestion and packet drops
  Susceptibility to denial of service

## Slide 39: Synchronization of Flows
Ideal bandwidth sharing
cwnd
cwnd
cwnd
Oscillating, but high overall utilization
In reality, flows synchronize
One flow causes all flows to drop packets
Periodic lulls of low utilization
Solved in IP routers using Random Early Detection (RED)
Also known as Random Early Drop

## Slide 40: Small Flows
Problem: TCP is biased against short flows
  1 RTT wasted for connection setup (SYN, SYN/ACK)
  cwnd always starts at a low number (originally, 1)
Vast majority of Internet traffic is short flows
  Mostly HTTP transfers, <100KB
  Most TCP flows never leave slow start!
Proposed solutions
  Increase initial cwnd to a larger value, e.g., 64
  TCP Fast Open: use cryptographic hashes to identify receivers, eliminate the need for three-way handshake

## Slide 41: Initial Window Size
What should be the initial value of cwnd?
  Too small – flows take longer to leave slow start
  Too big – new flows create burst of traffic that may congest networks
Subject of ongoing debate
  E.g., Linux kernel officially adopted cwnd = 10 in 2011
What sizes are in use today?
Jan Rüth, Christian Bormann, Oliver Hohlfeld. Large-scale Scanning of TCP’s Initial Window. IMC 2017.

## Slide 42: High Bandwidth-Delay Product
Key Problem: TCP performs poorly when
  The capacity of the network (bandwidth) is large, or
  The delay (RTT) of the network is large, or
  The bandwidth-delay product is large
Why does TCP perform poorly?
  Slow start and additive increase are slow to converge when bandwidth is large
  TCP is ACK clocked
    i.e., TCP can only react as quickly as ACKs are received
    Large RTT  ACKs are delayed  TCP is slow to react

## Slide 43: Poor Performance of TCP Reno
Bottleneck Bandwidth (Mb/s)
Avg. TCP Utilization
50 flows in both directions
Buffer = BW x Delay
RTT = 80 ms
Round Trip Delay (sec)
Avg. TCP Utilization
50 flows in both directions
Buffer = BW x Delay
BW = 155 Mb/s

## Slide 44: How to Improve Utilization?
Fast window growth
  Slow start and additive increase are too slow when bandwidth is large
  Want to converge more quickly
Maintain fairness with other TCP variants
  Window growth cannot be too aggressive
Simple implementation

## Slide 45: Compound TCP Implementation
Default TCP implementation in Windows
Key idea: split cwnd into two separate windows
  Traditional, loss-based window
  New, delay-based window
wnd = min(cwnd + dwnd, adv_wnd)
  cwnd is controlled by AIMD
  dwnd is the delay window
Rules for adjusting dwnd:
  If RTT is increasing, decrease dwnd (dwnd >= 0)
  If RTT is decreasing, increase dwnd
  Increase/decrease are proportional to the rate of change

## Slide 46: Compound TCP Example
RTT
Decreasing
RTT
Increasing
Aggressiveness corresponds to changes in RTT
Advantages: fast ramp up, fairer to flows with different RTTs
Disadvantage: must estimate RTT, which is very challenging
Time
cwnd
Timeout
Slow Start
Timeout
Slower cwnd growth
Faster cwnd growth

## Slide 47: TCP CUBIC Implementation
Default TCP implementation in Linux
Replace AIMD with cubic function
  C  a constant scaling factor
  β  a constant fraction for multiplicative decrease
  T  time since last packet drop
  cwndmax  cwnd when last packet dropped

## Slide 48: TCP CUBIC Example
Less wasted bandwidth due to fast ramp up
Stable region and slow acceleration help maintain fairness
  Fast ramp up is more aggressive than additive increase
  To be fair to Tahoe/Reno, CUBIC needs to be less aggressive
Time
cwnd
Timeout
Slow Start
CUBIC Function
cwndmax
Fast ramp up
Stable
Region
Slowly accelerate to probe for bandwidth

## Slide 49: Simulations of TCP Flows
CUBIC
CUBIC
Reno
Reno
Unfairness between TCP variants that share a link
CUBIC is more aggressive, so obtains an unfair bandwidth share

## Slide 50: Deploying TCP Variants
TCP assumes all flows employ TCP-like congestion control
  TCP-friendly or TCP-compatible
  Violated by UDP :(
If new congestion control algorithms are developed, they must be TCP-friendly
Be wary of unforeseen interactions
  Variants work well with others like themselves
  Different variants competing for resources may trigger unfair, pathological behavior

## Slide 51: Outline
Congestion Basics
Original TCP
TCP Tahoe and Reno
TCP Cubic
BBR

## Slide 52: Issues with TCP
Most Internet traffic is TCP
However, many issues with the protocol
  Synchronization of flows
  Poor performance with small flows
  Problems on modern, high bandwidth-delay product networks
    Slow ramp-up when bandwidth is large, low utilization
  Lack of fairness when RTT varies across flows
  Poor performance on wireless networks, packet loss is assumed to be congestion
  Probing for bandwidth induces congestion and packet drops
  Susceptibility to denial of service
Random Early Drop/Detection in IP routers
Increase initial cwnd
CUBIC instead of AIMD

## Slide 53: Fairness
Key problem: TCP throughput depends on RTT
1 Mbps
1 Mbps
1 Mbps
1 Mbps
1 Mbps
100 ms
1000 ms
ACK clocking makes TCP inherently unfair
Possible solution: explicitly take changes in delay (RTT) into account
  Implemented by Microsoft’s Compound TCP and Google’s BBR

## Slide 54: Wireless Networks
Problem: Tahoe and Reno assume loss = congestion
  True on the WAN, bit errors are very rare
  False on wireless, interference is very common
TCP throughput ~ 1/sqrt(drop rate)
  Even a few interference drops can kill performance
Possible solutions:
  Break layering, push data link info up to TCP
  Explicit congestion notification (ECN)
    Routers mark the 1-bit ECN field in the TCP header to indicate congestion
  Use delay-based congestion detection (TCP Vegas, BBR)

## Slide 55: TCP BBR
Motivation: Loss does not always imply congestion
Bottleneck Bandwidth and Round-trip (BBR)
Key idea: model the bottleneck bandwidth rate using two properties
  Bottleneck bandwidth
  Propagation RTT
Based on the model, vary:
  The congestion window size
  The sending rate, i.e., how quickly segments are transmitted
Developed by Google, beginning in 2016

## Slide 56: TCP BBR v1 Goals
Don't overreact: don't do a multiplicative decrease on every round trip with loss/ECN
Probe robustly: try to probe beyond estimated max bandwidth before reducing the estimate
Grow scalably: start probing at 1 extra packet, grow exponentially to use free capacity
Loss != congestion, helps in wireless networks
Same as TCP Tahoe, Reno, Cubic
No additive increase; like slow start and CUBIC

## Slide 57: TCP BBR v2 Goals
All v1 goals, plus…
Leave headroom: leave space for entering flows to grab
Probe deferentially: probe on a time scale to allow coexistence with Reno/CUBIC
Avoid overshooting: start probing at an inflight measured to be tolerable
React quickly: using loss/ECN, adapt to delivery process now to maintain flow balance
Fairness towards less aggressive TCP variants
Fairness towards new flows
BBR v1 did not consider drops as a congestion signal at all; too aggressive

## Slide 58: Recall…The Danger of Increasing Load
Knee – point after which
  Throughput increases very slowly
  Delay increases quickly
In an M/M/1 queue
  Delay = 1/(1 – utilization)
Cliff – point after which
  Throughput  0
  Delay  ∞
Congestion Collapse
Load
Load
Goodput
Delay
Knee
Cliff
Ideal point

## Slide 59
Key idea: model the bottleneck bandwidth rate using two properties
  Bottleneck bandwidth (btlBw)
  Propagation RTT (RTprop)
  Bandwidth Delay Product (BDP) = btlBw × Rtprop
Measuring btlBw
  Finds maximum observed delivery rate over past 10 RTTs
  Periodically increases send rate to 1.25 × btlBw to search for more bandwidth
Measuring Rtprop
  Finds minimum RTT over past 10 seconds based on ACKs
  Problem: BBR may induce queueing delays by sending to fast
  Solution: periodically “drain” queues by sending at 25% less than btlBw
Send data so that one BDP of data is in flight at a time
  Send rate (pacing) limited by cwnd or pacing_rate (pacing_gain × btlBw)
  cwnd capped to 2 × BDP (to overcome delays in received acks)

## Slide 60: TCP BBR Example
RTT
Decr.
RTT
Incr.
Time
Sending Rate
Bottleneck
Bandwidth
Bottleneck
Bandwidth
STARTUP
DRAIN
PROBE_BW
PROBE_RTT

## Slide 61: BBR Outperforms CUBIC in the WAN
https://www.ietf.org/proceedings/97/slides/slides-97-iccrg-bbr-congestion-control-02.pdf

## Slide 62: Enable BBR For Yourself
On Linux, edit /etc/sysctl.conf and add:
    net.core.default_qdisc=fq
    net.ipv4.tcp_congestion_control=bbr
Run sysctl –p to reload the config
Check that it worked by running sysctl net.ipv4.tcp_congestion_control

## Slide 63: Outline
Bonus: SYN Cookies

## Slide 64: Denial of Service
Problem: TCP connections require state
  Initial SYN allocates resources on the server
  State must persist for several minutes (RTO)
SYN flood: send enough SYNs to a server to allocate all memory/meltdown the kernel
Solution: SYN cookies
  Idea: don’t store initial state on the server
  Securely insert state into the SYN/ACK packet
  Client will reflect the state back to the server

## Slide 65: SYN Cookies
Did the client really send me a SYN recently?
  Timestamp: freshness check
  Cryptographic hash: prevents spoofed packets
Maximum segment size (MSS)
  Usually stated by the client during initial SYN
  Server should store this value…
  Reflect the clients value back through them
Sequence Number
Timestamp
31
0
5
MSS
8
Crypto Hash of Client IP & Port

## Slide 66: SYN Cookies in Practice
Advantages
  Effective at mitigating SYN floods
  Compatible with all TCP versions
  Only need to modify the server
  No need for client support
Disadvantages
  MSS limited to 3 bits, may be smaller than clients actual MSS
  Server forgets all other TCP options included with the client’s SYN
    SACK support, window scaling, etc.