## Slide 1: CS 4700 Network Fundamentals
Inter Domain Routing
(It’s all about the Money)
Revised 10/2/25

## Slide 2: Network Layer, Control Plane
Function:
  Set up routes between networks
Key challenges:
  Implementing provider policies
  Creating stable paths
Application
Presentation
Session
Transport
Network
Data Link
Physical
BGP
RIP
OSPF
Control Plane
Data Plane

## Slide 3: Internet Routing
Internet organized as a two-level hierarchy
First level – autonomous systems (AS’s)
  AS – region of network under a single administrative domain
  Examples: Comcast, AT&T, Verizon, T-Mobile, etc.
  AS’s use intra-domain routing protocols internally
  Distance Vector, e.g., Routing Information Protocol (RIP)
  Link State, e.g., Open Shortest Path First (OSPF)
Connections between AS’s use inter-domain routing protocols
  Border Gateway Routing (BGP)
  De facto standard today, BGP-4

## Slide 4: ASs, Revisited
AS-1
AS-2
AS-3
Interior Routers
BGP Routers

## Slide 5: Why Do We Have ASs?
History – the Internet started as a network of networks
Routing algorithms are not efficient enough to execute on the entire Internet topology
Different organizations may use different routing policies
Allows organizations to hide their internal network structure
Allows organizations to choose how to route across each other (BGP)
Easier to compute routes
Greater flexibility
More autonomy/independence

## Slide 6: AS Numbers
Each AS identified by an ASN number
  Originally 16-bit values, expanded to 32 bits in 2006
  1023 are reserved for local/private use, 3 reserved for special use
Currently, there are ~ 70K advertised ASNs http://www.potaroo.net/tools/asn32/
  AT&T: 5074, 6341, 7018, …
  Sprint: 1239, 1240, 6211, 6242, …
  Northeastern: 156
  North America ASs  https://ftp.arin.net/info/asn.txt

## Slide 7: Inter-Domain Routing
Global connectivity is at stake!
  Thus, all ASs must use the same protocol
  Contrast with intra-domain routing (more on this later)
What are the requirements?
  Scalability
  Flexibility in choosing routes
    Cost
    Routing around failures
BGP is a Path Vector protocol
  BGP includes path information in protocol messages

## Slide 8: BGP
Border Gateway Protocol
  De facto inter-domain protocol of the Internet
  Policy based routing protocol
  Uses a Bellman-Ford path vector protocol
Relatively simple protocol, but…
  Complex, manual configuration
  Entire world sees advertisements
    Errors can screw up traffic globally
  Policies driven by economics
    How much $$$ does it cost to route along a given path?
    Not by performance (e.g. shortest paths)

## Slide 9: BGP Relationships
Customer
Provider
Customer pays provider
Peer 1
Peer 2
Peer 3
Peers do not pay each other
Peer 2 has no incentive to route 1 3
Customer
Customer
Provider

## Slide 10: Tier-1 ISP Peering
AT&T
Centurylink
Verizon Enterprise
NTT
Deutsche Telekom
Sprint
Orange

## Slide 11
Notes: From https://www.caida.org/projects/as-core/pics/2020/ascore-2020-ipv4-standalone.png

## Slide 12: Peering Wars
Reduce upstream costs
Improve end-to-end performance
May be the only way to connect to parts of the Internet
You would rather have customers
Peers are often competitors
Peering agreements require periodic renegotiation
Peer
Don’t Peer
Peering struggles in the ISP world are extremely contentious, agreements are usually confidential

## Slide 13: Two Types of BGP Neighbors
IGP
Exterior routers also speak IGP
eBGP
eBGP
iBGP
iBGP

## Slide 14: Full iBGP Meshes
Question: why do we need iBGP?
  Intra-network routing does not include BGP policy info
  Prevents routing loops within the AS
iBGP updates do not trigger announcements in the intra-network routing protocol
eBGP
iBGP

## Slide 15: Path Vector Protocol
AS-path: sequence of ASs a route traverses
  Similar to distance vector, but sends the entire path
Used for loop detection and to apply policy
  If you see your own ID in an advertisement, discard it
Default choice: route with fewest # of ASs
110.10.0.0/16
AS 1
AS 2
130.10.0.0/16
AS 3
120.10.0.0/16
AS 4
AS 5
120.10.0.0/16: AS 2  AS 3  AS 4
130.10.0.0/16: AS 2  AS 3
110.10.0.0/16: AS 2  AS 5
110.10.0.0/16: AS2  AS3  AS4  AS5
120.10.0.0/16: AS4
120.10.0.0/16: AS3  AS4
120.10.0.0/16: AS2  AS3  AS4

## Slide 16: BGP Operations (Simplified)
Establish session on TCP port 179
Exchange active routes
Exchange incremental updates
AS-1
AS-2
BGP Session

## Slide 17: Four Types of BGP Messages
Open: Establish a peering session.
Keep Alive: Handshake at regular intervals.
Notification: Shuts down a peering session.
Update: Announce new routes or withdraw previously announced routes.
announcement = IP prefix + attributes values

## Slide 18: CS 4700 ECON 4700 Network Fundamentals
Inter Domain Routing
(It’s all about the Money)

## Slide 19: BGP Attributes
Some attributes used to select “best” path
  LocalPref
    Local preference policy to choose most preferred exit path
    Overrides default fewest AS behavior
  Multi-exit Discriminator (MED)
    Chooses peering point to your network from your neighbor
    Specifies path for external traffic destined for an internal network
Relationships control how routes are shared with others
  Import Rules
    What route advertisements do I accept?
  Export Rules
    Which routes do I forward to whom?

## Slide 20: Route Selection Summary
Highest Local Preference
Shortest AS Path
Lowest MED
Lowest IGP Cost to BGP Egress
Lowest Router ID
Traffic engineering
Enforce relationships
When all else fails,
break ties

## Slide 21: Shortest AS Path != Shortest Path
Source
Destination
?
?
4 hops
4 ASs
9 hops
2 ASs

## Slide 22: Hot Potato Routing
Destination
Source
3 hops total,
2 internal hops
?
?
5 hops total, 1 internal hop

## Slide 23: BGP Attributes Revisited
BGP relationships control how routes are shared with others
Import Rules
  What route advertisements do I accept?
Export Rules
  Which routes do I forward to whom?

## Slide 24: Importing Routes
From Provider
From Peer
From Peer
From Customer
ISP Routes

## Slide 25: Exporting Routes
To Customer
To Peer
To Peer
To Provider
Customers get all routes
Customer and ISP routes only
$$$ generating routes

## Slide 26: AS Relationships: It’s Complicated
Typical models of AS relationships are simple
  Each AS pair has exactly one relationship
  Each relationship is the same for all prefixes
Unfortunately, in practice it’s much more complicated
  Widespread regional, per-prefix peerings
  Tier-1’s being shoved out by “hypergiant” content providers
  Internet Exchange Points (IXPs) dominating traffic volume

## Slide 27: Project 4
If you haven’t started yet, today is a good day to begin.

## Slide 28: BGP Security
BGP is insecure by default
  Any trusted BGP router may announce any route
  Prefix hijacking is entirely possible
Examples
  2008: YouTube accidentally blocked globally by an ISP in Pakistan
  2022: KLAYswap crypto phishing attack in South Korea
Resource Public Key Infrastructure (RPKI)
  All route announcements are cryptographically signed
  Public binding between cryptographic keys and prefixes
  However, only ~30% adoption so far

## Slide 29: CS 4700 Network Fundamentals
Bonus: 2021 Facebook Outage

## Slide 30: The Outage
Gather round, we’ll cover an event, quite sober
One that took place on the fourth of October
Facebook, Insta, and friends couldn’t be reached
Rumors spread that the service was breached
At the datacenter keycards were denied
In fact, all the recovery systems were fried
At last, on doors angle grinders were employed
To fix a network config erroneously deployed
Six hours of downtime committed to lore:
For Facebook was thwarted by BGP4

## Slide 31: Ripped from the headlines

## Slide 32: Diagnosing an outage
FB, Insta, WhatsApp down
Was it DNS?
  Wait, DNS is unreachable?
No routing table entries?
Could it be … BGP?

## Slide 33: What happened?
15:39 UTC: Routes to Facebook became unavailable
Shortly thereafter: DNS entries timed out, lookups failed
Remote access to datacenters went down
Engineers deployed to datacenters to fix
  Keycard authentication relied on systems that were down
  Communication with people with keys went down
  Angle grinders were acquired
20:50 UTC: Routes re-established
21:05 UTC: DNS started working

## Slide 34: How routing tables are populated
Comcast
Tata
GTT
Lumen
Sprint
L3
Verizon
ATT
Charter
NU
FB
FB backbone
185.89.218.0/23: FB
185.89.218.0/23: FB
185.89.218.0/23: FB
185.89.218.0/23: VZ FB
185.89.218.0/23: ATT FB
185.89.218.0/23: GTT VZ FB
185.89.218.0/23: L3 ATT FB
185.89.218.0/23: Comcast L3 ATT FB
185.89.218.0/23: GTT VZ FB

## Slide 35: How routing tables adapt to outages
Comcast
Tata
GTT
Lumen
Sprint
L3
Verizon
ATT
Charter
NU
FB
FB backbone
185.89.218.0/23: FB
185.89.218.0/23: FB
185.89.218.0/23: FB
185.89.218.0/23: VZ FB
185.89.218.0/23: ATT FB
185.89.218.0/23: GTT VZ FB
185.89.218.0/23: L3 ATT FB
185.89.218.0/23: Comcast L3 ATT FB
185.89.218.0/23: GTT VZ FB
185.89.218.0/23: Comcast L3 ATT FB

## Slide 36: The great withdrawal

## Slide 37: The great withdrawal

## Slide 38: Root cause?

## Slide 39: Lessons learned
Vint Cerf: Internet is resilient to a nuclear holocaust
  Reality: Centralization among hypergiants reduces resilience
Layering: Great for modularity Reality: A house of cards
Automation: Great way to avoid human error Reality: When mistakes happen, scale can be astronomical
FB SWEs: Boatloads of talent Reality: We all make mistakes, some of them bigger than others

## Slide 40: CS 4700 Network Fundamentals
Bonus 2: Network Neutrality

## Slide 41
Hush-a-phone – noise muffler for telephones
Subject of the landmark Hush-a-phone v. US court case of 1956

## Slide 42: Common Carriers
In exchange for monopoly over a physical resource, the owner of the resource must provide access to all (reasonable, legal) takers
  Telecommunications companies, e.g., AT&T
  Oil pipeline providers
  Freight and logistics companies
What about the internet?

## Slide 43: US FCC Classifications
Title I – information services
  Netflix, E-mail, SMS, etc.
Title II – common carriers
  Historically applied to telephone companies
ISPs were regulated under Title I until 2015, then Title II
Switched back to Title I in 2018
Individual state laws and Pres. Exec order requests FCC to reinstate Title II
2025 Fed appeals court prohibits FCC to reinstate rules, citing 2024 Supreme Court decision limiting fed agencies (FCC)

## Slide 44: Why Does Classification Matter?
Blocking and throttling
  In the ‘90s and early 2000’s, ISPs routinely blocked apps like BitTorrent
  Cell network ISPs routinely slow down audio and video streams to force them to lower quality
Paid prioritization
  Cell networks charge extra for access to high-quality streaming video
  ISPs have demanded huge fees from content providers like Netflix
Zero rating
  AT&T lets you stream HBO Max (when it was owned by AT&T) at high-quality without impacting your monthly data limit
  Facebook subsidizes internet access in developing countries, but only for Facebook services

## Slide 45: Network Neutrality
Coined by Columbia Law professor Tim Wu
“All Internet traffic should be treated equally”
Dumb pipes – ISPs provide packet delivery and that is it

## Slide 46: Net Neutrality Rules
No blocking
ISP cannot arbitrarily censor websites, content, packets, etc.
Except to comply with other laws, e.g. copyright and anti-child porn, etc.
No throttling
ISP cannot arbitrarily slow down particular services
Exceptions for “reasonable network management”, cybersecurity, etc.
No paid prioritization
ISP cannot charge service providers for improved access to customers
No zero rating
ISP cannot give preference to some services by making them “free”
E.g. exempting a service from monthly data usage limits

## Slide 47: Measuring Net Neutrality Violations
Wehe app (iOS, Android)
  Developed at NU
  More than 2M tests to date
Nearly all US cell providers throttle video
  Not all video is throttled
  YouTube almost always is
  Vimeo less so
For more info, see wehe.meddle.mobi
  Run tests
  Play with public dataset