## Slide 1: CS 4700 Fundamentals of Computer Networks
Physical Layer
(The layer for EE majors…)
Revised 1/9/25

## Slide 2: Physical Layer
Function:
  Get bits across a physical medium
Key challenge:
  How to represent bits in analog
    Digital computers work in binary
    … but we live in an analog world
  Ideally, want high-bit rate
  But, must avoid desynchronization
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 3: Let’s Get Digital
Digital computers
  0s and 1s
Analog world
  Amplitudes and frequencies

## Slide 4: Assumptions
We have two discrete signals, high and low, to encode 1 and 0
Transmission is synchronous, i.e. there is a clock that controls signal sampling
Amplitude and duration of signal must be significant
Time
Sample

## Slide 5: Non-Return to Zero (NRZ)
1  high signal, 0  low signal
Clock
NRZ
0
0
0
0
0
0
1
1
1
1
Problem: long strings of 0 or 1 cause desynchronization
  How to distinguish lots of 0s from no signal?
  How to recover the clock during lots of 1s?

## Slide 6: Desynchronization
Problem: how to recover the clock during sequences of 0’s or 1’s?
NRZ
0
0
1
1
1
1
1
1
1
1
Transitions signify the senders clock ticks
0
0
1
1
1
1
1
1
1
Receiver misses a 1 due to skew
Sent Bits
Received Bits

## Slide 7: Non-Return to Zero Inverted (NRZI)
1  make transition, 0  remain the same
Clock
NRZI
0
0
0
0
0
0
1
1
1
1
Solves the problem for sequences of 1s, but not 0s

## Slide 8: 4-bit/5-bit (100 Mbps Ethernet)
Observation: NRZI works as long as no long sequences of 0
Idea: encode all 4-bit sequences as 5-bit sequences with no more than one leading 0 and two trailing 0
Tradeoff: efficiency drops to 80%
0000 11110
0001 01001
0010 10100
0011 10101
0100 01010
0101 01011
0110 01110
0111 01111
1000 10010
1001 10011
1010 10110
1011 10111
1100 11010
1101 11011
1110 11100
1111 11101
4-bit 5-bit
4-bit 5-bit
8-bit / 10-bit used in Gigabit Ethernet

## Slide 9: Manchester
1  high-to-low, 0  low-to-high
Clock
NRZI
0
0
0
1
1
Good: Solves clock skew (every bit is a transition)
Bad: Halves throughput (two clock cycles per bit)

## Slide 10: General Comments
Physical layer is the lowest, so…
  We tend not to worry about where to place functionality
  There aren’t other layers that could interfere
  We tend to care about it only when things go wrong
Physical layer characteristics are still fundamentally important to building reliable Internet systems
  Insulated media vs. wireless
  Packet vs. circuit switched media