## Slide 1: CS 4700 Network Fundamentals
Transport Layer
(UDP, but mostly TCP)
Revised 2/13/25

## Slide 2: Transport Layer
Function:
  Demultiplexing of data streams
Optional functions:
  Creating long lived “connections”
  Reliable, in-order packet delivery
  Error detection
  Flow and congestion control
Key challenges:
  Detecting and responding to congestion
  Balancing fairness against high utilization
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 3: Outline
UDP
TCP
  Header Format, Semantics
  Connection Lifecycle, Sequence Numbers
  Error Detection and Recovery
  TCP Options

## Slide 4: The Case for Multiplexing
Datagram network
  No circuits
  No connections
Clients run many applications at the same time
  Who to deliver packets to?
IP header “protocol” field
  8 bits = 256 concurrent streams
Insert Transport Layer to handle demultiplexing
Packet
Network
Data Link
Physical
Transport

## Slide 5: Demultiplexing Traffic
Endpoints identified by <src_ip, src_port, dest_ip, dest_port>
Network
Transport
Application
P1
P2
P3
P4
P6
P7
P5
Host 1
Host 2
Host 3
Unique port for each application
Applications share the same network
Server applications communicate with multiple clients

## Slide 6: Layering, Revisited
Application
Transport
Network
Data Link
Physical
Host 1
Router
Host 2
Physical
Lowest level end-to-end protocol (in theory)
  Transport header only read by source and destination
  Routers view transport header as payload
Application
Transport
Network
Data Link
Physical
Network
Data Link
Layers communicate peer-to-peer

## Slide 7: User Datagram Protocol (UDP)
Simple, connectionless datagram
  C sockets: SOCK_DGRAM
Port numbers enable demultiplexing
  16 bits = 65535 possible ports
  Port 0 is invalid
Checksum for error detection
  Detects (some) corrupt packets
  Does not detect dropped, duplicated, or reordered packets
Destination Port
0
16
31
Payload Length
Source Port
Checksum

## Slide 8: Usage Example
import socket
sock = socket.socket(socket.AF_INET, socket.SOCK_DGRAM)
sock.sendto(“message”, (“127.0.0.1”, 3456))
import socket
sock = socket.socket(socket.AF_INET, socket.SOCK_DGRAM)
sock.bind((“0.0.0.0”, 3456))
data, addr = sock.recvfrom(65535)
Sending on a client socket
Receiving on a server socket
No “connection”, UDP sockets are mostly stateless.
One UDP socket may send to many destinations.
OS needs to be told what port this application is listening to
One UDP socket may receive from multiple destinations
Notes: bind() semantic for 0.0.0.0 or “” for address -> bind to all known interfaces

## Slide 9: UDP Socket Semantics
sock.sendto(msg1, destination)
sock.sendto(msg2, destination)
sock.sendto(msg3, destination)
Src Prt
Dst Prt
msg1
Src Prt
Dst Prt
msg2
Src Prt
Dst Prt
msg3
Sending
Receiving
data, addr = sock.recvfrom(2048) #msg1
data, addr = sock.recvfrom(2048) #msg2
data, addr = sock.recvfrom(2048) #msg3
UDP Header
Datagram 1:
Datagram 2:
Datagram 3:

## Slide 10: UDP Socket Semantics
Sending a buffer will produce exactly one datagram containing the data from the buffer
  Warning: UDP datagrams may hold up to ~65,000 bytes of data…
  If len(UDP datagram) > MTU, IP will need to fragment it [avoid doing this]
Receiving will return exactly one, full datagram
  Not a partial datagram, not >1 datagrams

## Slide 11: Uses for UDP
Invented after TCP
  Why?
Not all applications can tolerate TCP
Custom protocols can be built on top of UDP
  Reliability? Strict ordering?
  Flow control? Congestion control?
Examples
  RTMP – real-time media streaming (e.g. voice, video)
  uTP – “microtransport” protocol used by BitTorrent
  QUIC – app-level transport protocol developed by Google to speed up HTTP

## Slide 12: Outline
UDP
TCP
  Header Format, Semantics
  Connection Lifecycle, Sequence Numbers
  Error Detection and Recovery
  TCP Options

## Slide 13: Transmission Control Protocol
Options
Reliable, in-order, bi-directional byte streams
  Port numbers for demultiplexing
  Virtual circuits (connections)
  Flow control
  Congestion control, approximate fairness
Destination Port
0
16
31
Sequence Number
Source Port
Acknowledgement Number
Advertised Window
Urgent Pointer
Flags
Checksum
4
HLen

## Slide 14: TCP Header Fields
Options
Destination Port
0
16
31
Sequence Number
Source Port
Acknowledgement Number
Advertised Window
Urgent Pointer
Flags
Checksum
4
HLen
Used to detect out of order, duplicate, and missing packets
Header length. Default length is 20 bytes, but may be longer with options.
Not used.
Used for flow control (protecting the receiver from overloading)
Used for connection establishment (SYN), acknowledgement (ACK), connection close (FIN), and errors (RST).

## Slide 15: Usage Example
import socket
sock = socket.socket(socket.AF_INET, socket.SOCK_STREAM)
sock.connect((“127.0.0.1”, 3456))
sock.sendall(“message”)
import socket
sock = socket.socket(socket.AF_INET, socket.SOCK_STREAM)
sock.bind((“0.0.0.0”, 3456))
sock.listen()
conn, addr = sock.accept()
data = conn.recv(2048)
Sending on a client socket
Receiving on a server socket
TCP is stateful, connections must be formed
One TCP socket only sends over one connection
OS needs to be told what port this application is listening to
Socket “listens” for incoming connections
Accept spawns a second socket
Notes: connect() has parameters for destination address and port. The OS specified the source versions: local address, an unused port on the system

## Slide 16: TCP Socket Semantics
sock.send(msg1)
sock.send(msg2)
sock.send(msg3)
Src Prt
Dst Prt
msg1
Src Prt
Dst Prt
msg2
Src Prt
Dst Prt
msg3
Sending
TCP Header
Segment 1:
Segment 2:
Segment 3:
Src Prt
Dst Prt
msg1 + msg2 + msg3
Segment 1:
Src Prt
Dst Prt
msg1 + msg2a
Src Prt
Dst Prt
msg2b + msg3
Segment 1:
Segment 2:

## Slide 17: TCP Socket Semantics
sock.send(msg1)
sock.send(msg2)
sock.send(msg3)
msg1
msg2
msg3
Sending
Receiving
data = sock.recv(2048)

## Slide 18: TCP Socket Semantics
Sending a buffer may produce any number of segments
  In practice, TCP tries to optimize by putting close to 1460 bytes in each segment
  But this is not true under all circumstances
Receiving may return any number of data bytes
  Could return part of a segment…
  Or a full segment…
  Or multiple segments…

## Slide 19: Phases of TCP
Connection setup, a.k.a. the three-way handshake
  Establish connection state
Data transfer
  Sequence numbers for reliable, in-order delivery
  Perform flow control
Connection close
  Free resources

## Slide 20: Connection Setup
Why do we need connection setup?
  To establish state on both hosts
  Most important state: sequence and acknowledgement numbers
    Count the number of bytes that have been sent
    Initial value chosen at random
    Why?
Important TCP flags (1 bit each)
  SYN – synchronization, used for connection setup
  ACK – acknowledge received data
  FIN – finish, used to tear down connection

## Slide 21: Three Way Handshake
Each side:
  Notifies the other of starting sequence number
  ACKs the other side’s starting sequence number (+1)
  Sequence # must increment on receiving a SYN
Client
Server
<SYN, Seq # C, Ack # ?>
<SYN/ACK, Seq # S, Ack # C+1>
<ACK, Seq # C+1, Ack # S+1>
Seq #
Ack#
Seq #
Ack #
C
?
S
C+1
C+1
S+1
S+1
C+1
Why
Sequence # +1?
Notes: 211

## Slide 22: Why Random Initial Sequence Numbers?
Connection confusion
  How to disambiguate connections from the same host?
  Random sequence numbers
Preventing packet injection
  How Kevin Mitnick hacked into the SDSC
  Need good random number generators!
Connection state management
  Each SYN allocates state on the server
  SYN flood is a common denial of service attack
  Solution: SYN cookies

## Slide 23: Phases of TCP
Connection setup, a.k.a. the three-way handshake
  Establish connection state
Data transfer
  Sequence numbers for reliable, in-order delivery
  Perform flow control
Connection close
  Free resources

## Slide 24: Data Transfer
TCP uses a byte stream abstraction
  Initial, random values selected during setup
  Each byte in each stream is numbered
  32-bit value, wraps around
Byte stream broken down into segments (packets)
  Size limited by the Maximum Segment Size (MSS, typically 1460 bytes)
  Set to limit fragmentation
Each segment has a sequence number
Segment 8
Segment 9
Segment 10
13450
14950
16050
17550
Byte stream to send

## Slide 25: Bidirectional Communication
Each side of the connection can send and receive
  Different sequence numbers for each direction
Client
Server
<Seq # 7, Ack # 23> 1460 data bytes
<ACK, Seq # 23, Ack # 1467> 730 data bytes
<ACK, Seq # 1467, Ack # 753> 1460 data bytes
Seq #
Ack#
Seq #
Ack #
7
23
23
1467
1467
753
753
2927
23
7
<ACK, Seq # 753, Ack # 2927> 240 data bytes
2927
993
Data and ACK in the same packet
Problem: this depicts a stop-and-wait protocol
Will not be able to utilize all available bandwidth

## Slide 26: Review from Layer 2: Stop and Wait Protocol
Simplest form of reliability
  Example: Bluetooth
Problems?
  Low utilization: can only have one segment in flight at any time
10Gbps link and 10ms delay
  Need 100 Mb to fill the pipe
  Assume packets are 1500B
1500B * (8b/1B) / 2 = 6000b = 0.006Mb
Utilization is 0.006%
Sender
Receiver
Segment
ACK
Timeout
Segment
Timeout
Retransmit Segment
Notes: 10ms is one-way delay.
Assume path is symmetrical. 2*10ms is round trip time.
Can only send next packet after ACK is received.

## Slide 27: Review from Layer 2: Sliding Window
Allow multiple outstanding, un-ACKed segments
Number of un-ACKed segments is called the window
Sender
Receiver
Segments
ACKs
Window
Made famous by TCP

## Slide 28: Flow Control
Problem: how big should the window be?
  Too many packets may overwhelm the receiver
  Size of the receiver's buffers may change over time
Solution: advertised window
  Receiver tells the sender how big their buffer (the window) is
  For window size n, sender may transmit n bytes without receiving an ACK
  After each ACK, the window slides forward
Advertised window may go to zero!

## Slide 29: Flow Control: View from the Sender Side
Sequence Number
Src. Port
Acknowledgement Number
Adv. Window
Urgent Pointer
Flags
Checksum
HL
Packet Sent
Dest. Port
Src. Port
Acknowledgement Number
Adv. Window
Urgent Pointer
Flags
Checksum
HL
Packet Received
Dest. Port
Sequence Number
ACKed
Sent
To Be Sent
Outside Window
Window
sock.send()
Must be buffered until ACKed
Buffer of Bytes to Send
Notes: Each side acts and sender and receiver
Every message contains sequence number, even if payload length is zero
Every message contains acknowledgements, even if no data was received
Every message advertises the window size

## Slide 30
Sliding Window Example
Buffer of Bytes to Send
Window = 3* MSS
Client
Server
<Seq # 7> 1460 data bytes
Seq #
Ack#
Seq #
Ack #
7
23
23
1467
23
2927
23
7
1460
1460
1460
1460
1460
1460
1460
<Seq # 1467> 1460 data bytes
<Seq # 2927> 1460 data bytes
23
4387
<ACK, Ack # 1467>
<ACK, Ack # 2927>
<ACK, Ack # 4387>
23
5847
23
7307
23
8767
<Seq # 4387> 1460 data bytes
<Seq # 5847> 1460 data bytes
<Seq # 7307> 1460 data bytes
1467
23
2927
23
4387
23

## Slide 31: What Should the Receiver ACK?
ACK every packet
Use cumulative ACK, where an ACK for sequence n implies ACKS for all k < n
Use negative ACKs (NACKs), indicating which packet did not arrive
Use selective ACKs (SACKs), indicating those that did arrive, even if not in order
  SACK is an actual TCP extension

## Slide 32: Sequence Numbers, Revisited
32 bits, unsigned
  Why so big?
To avoid acknowledgement ambiguity in the window you need…
  |Sequence # Space| >= 2 * |Sending Window Size|
  232 > 2 * 216

## Slide 33
Ambiguous Window Example
Client
<Seq # 0>
<Seq # 1>
<Seq # 0>
<ACK, Ack # 0>
Imagine that sequence numbers are 1-bit
  Segments are numbered zero or one
Assume window size = 3 segments
Which segment was acknowledged?

## Slide 34: Phases of TCP
Connection setup, a.k.a. the three-way handshake
  Establish connection state
Data transfer
  Sequence numbers for reliable, in-order delivery
  Perform flow control
Connection close
  Free resources

## Slide 35: Connection Tear Down
Either side can initiate tear down
Other side may continue sending data
  Half open connection
  shutdown()
Acknowledge the last FIN
  Sequence number + 1
Client
Server
<FIN, Seq # X, Ack # Y>
<ACK, Seq # Y, Ack # X+1>
<ACK, …>
<…> Data
<FIN, Seq # Z, Ack # X+1>
<ACK, Seq # X+1, Ack # Z+1>

## Slide 36: Error Detection and Recovery in TCP

## Slide 37: Error Detection
Checksum detects (some) packet corruption
  Computed over IP header, TCP header, and data
  Corrupt packets are dropped
Sequence numbers catch sequence problems
  Duplicates are ignored
  Out-of-order packets are reordered or dropped

## Slide 38
Out-of-Order (OoO) Delivery Example
Client
Server
<Seq # 7>
Seq #
Ack#
Seq #
Ack #
7
23
23
1467
23
1467
23
7
<Seq # 1467>
<Seq # 2927>
23
4387
<ACK, Ack # 1467>
<ACK, Ack # 1467>
<ACK, Ack # 4387>
23
5847
23
7307
23
8767
<Seq # 4387>
<Seq # 5847>
<Seq # 7307>
1467
23
1467
23
4387
23
Assume windows size = 3, all segments contain 1460 bytes of data
Assume OoO segments are buffered by the receiver
Ack # only increments in order
Duplicate ACK
Windows does not slide, no transmission
Ack # catches up by two segments
Window slides by two segments

## Slide 39
Packet Loss Example
Client
Server
<Seq # 7>
Seq #
Ack#
Seq #
Ack #
7
23
23
1467
23
1467
23
7
<Seq # 1467>
<Seq # 2927>
<ACK, Ack # 1467>
<ACK, Ack # 1467>
23
1467
<Seq # 4387>
1467
23
1467
23
Assume windows size = 3, all segments contain 1460 bytes of data
Assume OoO segments are buffered by the receiver
Ack # only increments in order
Duplicate ACK
Window does not slide, no transmission
<ACK, Ack # 1467>
1467
23

## Slide 40
Client
Server
<Seq # 7>
Seq #
Ack#
Seq #
Ack #
7
23
23
1467
23
1467
23
7
<Seq # 1467>
<Seq # 2927>
<ACK, Ack # 1467>
<ACK, Ack # 1467>
23
1467
<Seq # 4387>
1467
23
1467
23
<ACK, Ack # 1467>
1467
23
<Seq # 1467>
23
5847
5847
23
Window slides by three segments
Timeout, retransmit
<Seq # 2927>
<Seq # 4387>
<ACK, Ack # 5847>

## Slide 41: Error Detection
Checksum detects (some) packet corruption
  Computed over IP header, TCP header, and data
  Corrupt packets are dropped
Sequence numbers catch sequence problems
  Duplicates are ignored
  Out-of-order packets are reordered or dropped
Lost segments detected by sender
  Use timeout to detect lost segments and missing ACKs
  Need to estimate RTT to calibrate the timeout
  Sender must keep copies of all data until ACK

## Slide 42: Retransmission Time Outs (RTO)
Problem: time-out is linked to round trip time
Initial Send
ACK
Retry
RTO
Initial Send
ACK
Retry
RTO
Timeout is too short
What about if timeout is too long?

## Slide 43: Round Trip Time Estimation
Original TCP round-trip estimator
  RTT estimated as a moving average
  new_rtt = α (old_rtt) + (1 – α)(new_sample)
  Recommended α: 0.8-0.9 (0.875 for most TCPs)
RTO = 2 * new_rtt (i.e., TCP is conservative)
Data
ACK
RTT Sample

## Slide 44: RTT Sample Ambiguity
Karn’s algorithm: ignore samples for retransmitted segments
Initial Send
ACK
Retry
RTO
Initial Send
ACK
Retry
RTO
Sample
Sample?

## Slide 45: TCP Options

## Slide 46: Common TCP Options
Window scaling
Timestamp
SACK: selective acknowledgement
Maximum segment size (MSS)
Options
Destination Port
0
16
31
Sequence Number
Source Port
Acknowledgement Number
Advertised Window
Urgent Pointer
Flags
Checksum
4
HLen

## Slide 47: Utilization, Revisited
Sequence numbers are 32 bits, advertised windows are 16 bits
  The most data that can be in flight in parallel is 2^16 bytes
Recall that link capacity is measured by the bandwidth delay product
  bandwidth * delay = capacity
What is the maximum bandwidth TCP can utilize?
  100 ms of delay  2^16 bytes / 100 ms ~ 5 Kbps
  500 ms of delay  2^16 bytes / 500 ms ~ 1 Kbps
But ethernet scales to 1 Gbps, 10 Gbps, 100 Gbps…

## Slide 48: Window Scaling
Problem: the advertised window is only 16-bits
  Effectively caps the window at 65536 bytes, 64 KB
Solution: introduce a window scaling value
  scaled_adv_wnd = adv_wnd << wnd_scale;
  Maximum shift is 14 bits, 1GB maximum window

## Slide 49: Sequence Number Scaling
Problem: sequence numbers are only 32 bits
  Effectively caps the window at 2^32 ~ 4 GB
What is the maximum bandwidth TCP can utilize?
  100 ms of delay  2^32 bytes / 100 ms ~ 344 Mbps
  500 ms of delay  2^32 bytes / 500 ms ~ 69 Mbps
Solution: the PAWS algorithm
  32-bit timestamp option in TCP header
  When was the packet sent (approximately)
  Effectively extends the sequence numbers space to 64 bits

## Slide 50: SACK: Selective Acknowledgment
Problem: duplicate ACKs only tell us about 1 missing packet
  Multiple rounds of dup ACKs needed to fill all holes
Solution: selective ACK
  Include received, out-of-order sequence numbers in TCP header
  Explicitly tells the sender about holes in the sequence
8
9
10
11
3
4
5
6
7
3
3
3
3

## Slide 51: Other Common Options
Maximum segment size (MSS)
  Essentially, what is the hosts MTU
  Saves on path discovery overhead